Physics 313  Astrophysics		Spring 2009

Prof C. Hyde				chyde’@’odu.edu	www.odu.edu/~chyde/Teaching

Homework 6 Solution		due Wed March 18, 2009

- Use the web page www.nndc.bnl.gov/wallet/  ( or equivalent) to find the energy release in the following fusion reactions.

  - 4He + 12C ( 16O

  - 12C + 12C ( 24Mg

  - p + 12C ( 13N + g.

D(1H) = 7.289 MeV

D(4He) = 2.4249 MeV

D(12C) = 0.0  MeV

D(16O) = -4.7370 MeV

D(13N) =   MeV

D(24Mg) = -13.9330 MeV

D(4He)+ D(12C) - D(16O)=7.161 MeV

D(12C) D(12C) - D(24Mg) = 13.9330 MeV

D(1H)+ D(12C) - D(13N) = 1.944 MeV

- Astrophysics in a Nutshell Chapter 3 Problem 7.  
The nuclear reaction rate in a star is proportional to 

with

  - Show that the maximum value of f(E) occurs at

  - Form a Taylor series, to second order in ln[f(E)], to approximate f(E) as a Gaussian;  i.e. find A and  D in the approximation

Note that h( has units of 1/Energy2.

  - Using the Gaussian identities , show that   if E0>>D.

If E0>>D, then extending the lower limit to –infinity has negligible effect on the integral.  Change of variable to u=(E- E0)/ D :

- The pp chain produces 2 neutrinos for every 26.2 MeV of fusion energy release.  The solar flux of visible light reaching the upper atmosphere of the earth is ≈ 1000W/m2.  Assume the typical photon in the solar spectrum is a green photon of energy hv= 2 eV.

  - What is the number flux of visible photons reaching the upper atmosphere of the earth?	
Fg = P/(hv) = (1000 W/m2) / (2eV/photon),	
                    = [1000 (J/s(m2)] / (2 ( 1.6(10-19 C(V/photon),	
                    =  3.1 (1021 photon/( s(m2).

  - What is the number flux of neutrinos reaching the earth?	
Fn = P/(En) = (1000 W/m2) / (26.2MeV/2 neutrinos),	
                    = [1000 (J/s(m2)] / (13.1(106 (1.6(10-19 J/neutrino),	
                    =  48 (1013 neutrinos/( s(m2).

  - If the average energy of these neutrinos is 200 KeV, what fraction of the solar luminosity is carried away by neutrinos?	
fn = 2*200 KeV / (26.2 MeV) = 1.52%.

- Astrophysics in a Nutshell Chapter 3 Problem 8.
The power production per unit mass of the pp->De+n reaction is (3.134)

The “astrophysical S-factor” is S0=4(10-46 cm2 KeV.  For the first step in the chain, Q=2.2MeV, but for the whole pp chain Q= 26.2 MeV.  Use values from the solar center, r=150 g/cm3.

  - Perform dimensional analysis on the expression for e to establish it has units of Energy per unit mass per second.

Start with the argument of the exponential, kT has units of energy, so EG/kT is dimensionless.  The exponential is dimensionless.  All numerical factors are dimensionless.  Continue at the beginning r/MH has units of 1/Volume. S0c has units of Volume times energy per unit time, so
[r S0c /MH] has units of Energy per unit time, or Power.  Therefore [r S0c /MH2] has units of power per unit mass.  We just have to prove that the remaining factor is dimensionless.  This factor is Q(EG)1/6/[(Mc2)1/2(kT)2/3].  All of the factors are energy units, so the total dimension of this expression is energy to the power 1+1/6-1/2-2/3=0.

  - Approximate e as a power law .  Hint, make a Taylor series in lneas a function of ln(T/T0) and expand around ln(T/T0)=0.
First isolate the kT dependence in e:

Now take the logarithm,

re-express the last term as a function of  ln(kT/kT0)

For T near T0, ln (T/ T0) is close to 0.  Make a first order expansion of exp[-(1/3)ln(T/ T0)]:

  - Evaluate b for kT0=1.0 KeV and EG =500 KeV.